## Slide 1
Offline and Online UAV-Enabled Data Collection
in Time-Constrained IoT Networks
April 7, 2021
Under the supervision of
  Dr. Jihene Ben Abderrazak
  Dr. Wael Jaafar
Graduation Project
By
  Oussama Ghdiri
Notes: The obligation to reduce human contact as a health precaution has boosted the use of unmanned aerial vehicles It was really helpful for the human kind to overcome the pandemic. For instance

## Slide 2
Source: Cyient
Notes: The obligation to reduce human contact as a health precaution has boosted the use of unmanned aerial vehicles It was really helpful for the human kind to overcome the pandemic. For instance

## Slide 3
  We are just at the tip of the iceberg
  As a result, millions of people are profiting from UAVs
Notes:   Currently, the growth is in almost in every area creating new types of smart application and services

## Slide 4
  UAVs as Data collectors
Notes: In order, to undercover what the future might bring, we propose in this project to use UAVs as data collectors.

## Slide 5
1
2
3
4
Background & Motivation
Problem Formulation
Proposed Solution
Results and Discussion
5
Conclusions and Perspectives
  Presentation Outline

## Slide 6
Background & Motivation
1

## Slide 7
127 Devices every second*
* Source: McKinsey
** Source: Statista
25 in 2021**
Billion
  1, Background & Motivation
The vision of Internet of Things has been constantly expanding in every aspect of life
Generating an unprecedented amount of data
Notes: Globally, an estimated of 127 new devices connect to the Internet every second. Moreover, experts estimate that the number of active IoT devices will surpass 25 billion devices by the end of 2021. enabling promising IoT applications, connecting millions of devices and people and generating an unprecedented amount of data that can be used to unlock new levels of intelligence.

## Slide 8
  1, Background & Motivation
  Given that IoT devices might be deployed in hard-to-reach areas and over moving targets, collecting data from these IoT nodes in a timely manner becomes very challenging
  UAVs as flying data collectors has gained interest
    Flexibility
    Strong line-of-sight (LoS) communication channels
    Reach low-power IoT devices
Notes: Due to the UAVs’ high motion flexibility, strong line-of-sight (LoS) communication channels with ground devices, and moderately low flying altitudes to reach low-power IoT devices, UAV-based data collection is seen as the trigger of future and new applications

## Slide 9
  1, Background & Motivation
  State of the art
Notes: In our work we tried to overcome the weaknesses of the previous works and proposed a complete framework using Multi-UAV to collect data from IoT time constrained networks

## Slide 10
Problem Formulation
2

## Slide 11
  2, Problem Formulation
  System Model
Notes: To better understand the system model, we made this illustration . If you look at this figure you will see that we focus on collecting data from different heterogeneous sensors for example from autonomous cars, surveillance cameras, ,,,
whether in urban, suburban or rural env, we try to aggregate the data of those SNs into one super SN called CH and each CH has a specific deadline to before the data become outdated.

## Slide 12
Maximize energy efficiency
Maximize data collection
Ensure a successful communication between SN and CH
Guarantee that enough energy is available
Satisfy that UAV collects data from CHs before deadlines
Ensure that no collisions occurs between UAVs
  2, Problem Formulation
  Problem Formulation
Notes: The formulated optimization problem is determined by the following mathematical model.
The objective is to minimize the total energy consumption in the process of collecting data from CHs ensuring a successful communication between SN with their associated to CH using multiple UAVs that have enough on board battery capacity. So, the objective in to collect data from the maximum number of CHs before
information deadline. Which implies finding the most suitable trajectory guaranteeing that no collision occurs between UAVs.

## Slide 13
Proposed Solution
3

## Slide 14
  Problem P1 is divided into two sub-problems
    IoT sensors clustering
      Efficient SNs clustering
      Strategic CHs placement
    2. Multi-UAV Trajectory Planning
      Careful design of UAVs’ trajectories
      The offline scenario corresponds to applications for dedicated or private IoT networks
      The online scenario corresponds to applications where IoT sensors are mobile or their location information is fully or partially unavailable
  3, Proposed Solution

## Slide 15
  IoT sensors clustering (1/2)
    Partitioning methods
      Partition data into k subsets based on the characteristics and similarity of the data
    Used algorithms
      K-means
      Proposed K-means based algorithm
  3, Proposed Solution

## Slide 16
  IoT sensors clustering (2/2)
    Hierarchical methods
      Create a hierarchical decomposition of the data
      Represented graphically by a Dendrogram
    Used algorithms
      Hierarchical Agglomerative
      Clustering (HAC)
  3, Proposed Solution

## Slide 17
  Multi-UAV Trajectory Planning (1/6)
  Offline Path Planning: Meta-heuristic Approaches
      Graph-Based Approach
      Shortest path
      Vehicle Routing Problem with Time Windows
    Three metaheuristics algorithms :
        Guided local search
        Simulated annealing
        Tabu search
  3, Proposed Solution
Notes: Given the best location of CHs, we focus now on finding the UAV's appropriate path planning that may significantly decrease the energy consumption.
So we convert this problem into a graph so that we can find the best routes and by the best we mean the shortest path respecting deadline constraint.
Our approach is inspired from one of the most important applications of optimization which is vehicle routing problem with time-windows (VRPTW) to minimize the total flying distance and the number of UAVs needed to complete the mission.

## Slide 18
  Multi-UAV Trajectory Planning (2/6)
  Online Path Planning: Reinforcement-Learning based Approaches (1/5)
  3, Proposed Solution
Reinforcement learning is about solving problems by trial and error
Agent is an assumed entity which performs actions in an environment to gain some reward.
The Environment is the world that contains the agent and allows the agent to observe that world's state.
A state is a complete information description of the world
An observation is what the agent sees about the current state
Notes: So first just to get everybody on the same page the agent is

## Slide 19
  Multi-UAV Trajectory Planning (3/6)
  Online Path Planning: Reinforcement-Learning based Approaches (2/5)
  3, Proposed Solution
The Agent receives state st from the environment
Based on that state st, the agent takes an action at
The Environment gives some reward rt to the agent
The environment becomes in a new state st+1
This loop continues to form an Episode, which is a sequence of interaction between agent and environment.
Agent
Environment
State st
Action at
Reward rt

## Slide 20
  Multi-UAV Trajectory Planning (4/6)
  Online Path Planning: Reinforcement-Learning based Approaches (3/5)
    Value-based or Q-learning: Maximize a value function Q(s)
      Used algorithms
      DQN
      DDQN
    Policy-based: Optimize a policy π
      Used algorithms
      Actor-critic
  3, Proposed Solution

## Slide 21
  Multi-UAV Trajectory Planning (5/6)
  Online Path Planning: Reinforcement-Learning based Approaches (4/5)
    Trained a multi-task agent for 1024 episodes
    For each episode, we assume that the locations of SNs (and subsequently of CHs) are varying and unknown for the UAVs
    UAVs explore the cells and reach the CHs to collect the maximum amount of data within the time and energy limitations
  3, Proposed Solution

## Slide 22
  Multi-UAV Trajectory Planning (6/6)
  Online Path Planning: Reinforcement-Learning based Approaches (5/5)
    Exploration vs Exploitation
    Exploration is all about finding more information about an environment
    Exploration = less reward, but understand environment better
    Exploitation is exploiting already known information to maximize the rewards
    Exploration = more reward, may be missing out on a part of environment
    Trade-off between exploration and exploitation
  3, Proposed Solution

## Slide 23
Results and Discussion
4

## Slide 24
2000 SNs in 5x5 Km² area
Required number of CHs for different dth
Small dth  Higher number of CHs
Algo. 5 provides the best clustering performance
  Clustering performance (1/3)
  4, Results and Discussion

## Slide 25
  Clustering performance (2/3)
  4, Results and Discussion
Above Vs Within a range from CHs
Notes: Three combinations of IoT sensors clustering methods and UAVs’ hovering techniques

## Slide 26
Three combinations of IoT sensors clustering methods and UAVs’ hovering techniques
12 UAVs with 3500 mAh battery capacity
Collecting data within a range presents the best energy consumption performance
  Clustering performance (3/3)
  4, Results and Discussion

## Slide 27
  Offline path planning
Collecting data from 48 CHs with 140s deadline before data becomes outdated
Performances of these methods are almost similar, with a preference for Tabu
As the battery capacity increases the performance saturates, thus guaranteeing that data is collected from all CHs
  4, Results and Discussion

## Slide 28
  Online path planning (1/4)
3 UAVs with medium battery capacity
1800 SNs in 2000x2000 gridworld (2x2 Km²)
Collecting data from CHs with low deadlines
DQN and AC are faster to converge than DDQN
Actor-Critic achieves the best performance
  4, Results and Discussion

## Slide 29
  Online path planning (2/4)
Comparing the percentage of collected data between offline and online approaches
Tabu search performance is the benchmark
Using 3 UAVs we reached more than 95% of CHs
  4, Results and Discussion

## Slide 30
  Online path planning (3/4)
As the deadline increases, both AC and OFF improve until reaching a saturation value
OFF saturates from deadline 150sec, for which 100% of the data is collected
AC reaches a maximum of 90% starting from deadline 750sec
  4, Results and Discussion

## Slide 31
  Online path planning (4/4)
OFF reaches a consumption peak then decreases, mainly due to better UAV paths
AC consumes a lot of energy for short deadlines since the UAVs waste a lot of energy exploring without any income
This large gap is due to the advantageous knowledge of the system status
  4, Results and Discussion

## Slide 32
  List of Publications
    O. Ghdiri, W. Jaafar, S. Alfattani, J. B. Abderrazak and H. Yanikomeroglu, ”Energy-Eﬃcient Multi-UAV Data Collection for IoT Networks with Time Deadlines,” Proc. GLOBECOM 2020 - 2020 IEEE Global Communications Conference, Taipei, Taiwan, 2020
    O. Ghdiri, W. Jaafar, S. Alfattani, J. B. Abderrazak and H. Yanikomeroglu, ”Oﬄine and Online UAV-enabled Data Collection in Time constrained IoT Networks,” in IEEE Transactions on Green Communications and Networking - Special Issue - Selected papers from IEEE Globecom’20 (submitted)
  4, Results and Discussion

## Slide 33
Conclusions and Perspectives
5

## Slide 34
  Multi-UAV data collection problem in clustered IoT networks, where sensed data have time deadlines, was investigated
  Deployment energy costs were minimized through a two-step optimization approach:
    1) IoT sensors clustering and CHs optimal placement
    2) UAVs deployment and trajectories planning
  5, Conclusions and Perspectives
  Conclusions (1/2)

## Slide 35
  5, Conclusions and Perspectives
  Our customized K-means clustering method outperformed baseline approaches in terms of number of CHs
  Tabu search provided the best UAVs deployment strategies for energy minimization
  Actor-Critic outperforms DQN and DDQN in terms of amount of collected data and energy consumption
  Actor-Critic is capable of collecting up to 90% of the data without any prior knowledge of the IoT network
  Conclusions (2/2)

## Slide 36
  5, Conclusions and Perspectives
  In our future works, we plan to:
    Use energy harvesting
    Deploy mobile SNs
    Secure all data transactions
  Perspectives

## Slide 37
THANK YOU
ANY QUESTIONS?